## Slide 1: L10 Cache Optimizations Exercises
Zonghua Gu, 2018
4/30/2018
Acknowledgement: some slides taken from UC Berkeley CS61C

## Slide 2: Q1: Loop ordering
Consider the following two loops, which calculate the sum of the entries in a 128x64 matrix A of 32-bit integers:
Loop A | Loop B
sum = 0; for (i = 0; i < 128; i++) for (j = 0; j < 64; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 64; j++) for (i = 0; i < 128; i++) sum += A[i][j];
Matrix A is stored contiguously in memory in row-major order. Row major order means that elements in the same row of the matrix are adjacent in memory (A[i][j] resides in memory location [4*(64*i + j)]).
0 | 4 |  |  | 252 | 256 |  | 4*(64*127+63)
A[0][0] | A[0][1] |  | ... | A[0][63] | A[1][0] | ... | A[127][63]

## Slide 3: Q1.1: DM cache
Assume that the caches are initially empty. Only accesses to matrix A cause memory references and all other necessary variables are stored in registers. Instructions are in a separate instruction cache.
Consider a 4KB DM data cache with 32 Bytes/block. Calculate the number of cache misses for Loop A and Loop B.

## Slide 4: A1.1: DM Cache
Consider a 4KB DM cache with 32 Bytes/block. Total 128 blocks.
Matrix A has 128 rows and 64 columns. Each row has 64 32-bit (4B) integers and occupies (64*4/32)=8 cache blocks.
Loop A accesses memory sequentially (each iteration of Loop A sums a row in matrix A), an access to an int that maps to the first word in a cache line will miss (red words in the table) but the next 7 accesses will hit. Therefore, Loop A will only have compulsory misses, with total of 128*(64/8)=1024 misses.
B0 | A[0][0] | A[0][1] | A[0][2] | A[0][3] | A[0][4] | A[0][5] | A[0][6] | A[0][7]
B1 | A[0][8] | A[0][9] | A[0][10] | A[0][11] | A[0][12] | A[0][13] | A[0][15] | A[0][15]
B2 | A[0][16] | A[0][17] | A[0][18] | A[0][19] | A[0][20] | A[0][21] | A[0][22] | A[0][23]
B3 | A[0][24] | A[0][25] | A[0][26] | A[0][27] | A[0][28] | A[0][29] | A[0][30] | A[0][31]
B4 | A[0][32] | A[0][33] | A[0][34] | A[0][35] | A[0][36] | A[0][37] | A[0][38] | A[0][39]
B5 | A[0][40] | A[0][41] | A[0][42] | A[0][43] | A[0][44] | A[0][45] | A[0][46] | A[0][47]
B6 | A[0][48] | A[0][49] | A[0][50] | A[0][51] | A[0][52] | A[0][53] | A[0][54] | A[0][55]
B7 | A[0][56] | A[0][57] | A[0][58] | A[0][59] | A[0][60] | A[0][61] | A[0][62] | A[0][63]
B8 | A[1][0] | A[1][1] | A[1][2] | A[1][3] | A[1][4] | A[1][5] | A[1][6] | A[1][7]
Loop A | Loop B
sum = 0; for (i = 0; i < 128; i++) for (j = 0; j < 64; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 64; j++) for (i = 0; i < 128; i++) sum += A[i][j];
…

## Slide 5: A1.1: DM Cache
Consider a 4KB DM cache with 32 Bytes/block. Total 128 blocks.
Matrix A has 128 rows and 64 columns. Each row has 64 32-bit (4B) integers and occupies (64*4/32)=8 cache blocks.
Consecutive accesses in Loop B use every 8th cache block (B0, B8, B16…). When Loop B accesses a column, all the data that the previous iterations brought in earlier would have already been evicted. Thus, every access will cause a cache miss, with total of 128*64=8192 misses.
B0 | A[0][0] | A[0][1] | A[0][2] | A[0][3] | A[0][4] | A[0][5] | A[0][6] | A[0][7]
B1 | A[0][8] | A[0][9] | A[0][10] | A[0][11] | A[0][12] | A[0][13] | A[0][15] | A[0][15]
B2 | A[0][16] | A[0][17] | A[0][18] | A[0][19] | A[0][20] | A[0][21] | A[0][22] | A[0][23]
B3 | A[0][24] | A[0][25] | A[0][26] | A[0][27] | A[0][28] | A[0][29] | A[0][30] | A[0][31]
B4 | A[0][32] | A[0][33] | A[0][34] | A[0][35] | A[0][36] | A[0][37] | A[0][38] | A[0][39]
B5 | A[0][40] | A[0][41] | A[0][42] | A[0][43] | A[0][44] | A[0][45] | A[0][46] | A[0][47]
B6 | A[0][48] | A[0][49] | A[0][50] | A[0][51] | A[0][52] | A[0][53] | A[0][54] | A[0][55]
B7 | A[0][56] | A[0][57] | A[0][58] | A[0][59] | A[0][60] | A[0][61] | A[0][62] | A[0][63]
B8 | A[1][0] | A[1][1] | A[1][2] | A[1][3] | A[1][4] | A[1][5] | A[1][6] | A[1][7]
Loop A | Loop B
sum = 0; for (i = 0; i < 128; i++) for (j = 0; j < 64; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 64; j++) for (i = 0; i < 128; i++) sum += A[i][j];
…
Notes: 1 column of matrix A will occupy 128*8=1024 cache blocks, exceeding size of cache (128 blocks).

## Slide 6: Q1.2: DM Cache
Consider a DM cache with 32 Bytes/block. What is the minimum number of cache blocks required if Loop A is to run with only compulsory misses. What is the minimum number of cache blocks required if Loop B is to run with only compulsory misses.
Loop A | Loop B
sum = 0; for (i = 0; i < 128; i++) for (j = 0; j < 64; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 64; j++) for (i = 0; i < 128; i++) sum += A[i][j];

## Slide 7: A1.2: DM Cache
Since Loop A accesses memory sequentially, we can overwrite the cache blocks that were previous brought in. Loop A will only require 1 cache block to run without any cache misses other than compulsory misses.
B0 | A[0][0] | A[0][1] | A[0][2] | A[0][3] | A[0][4] | A[0][5] | A[0][6] | A[0][7]
Loop A | Loop B
sum = 0; for (i = 0; i < 128; i++) for (j = 0; j < 64; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 64; j++) for (i = 0; i < 128; i++) sum += A[i][j];
B0 | A[0][8] | A[0][9] | A[0][10] | A[0][11] | A[0][12] | A[0][13] | A[0][15] | A[0][15]
B0 | A[0][16] | A[0][17] | A[0][18] | A[0][19] | A[0][20] | A[0][21] | A[0][22] | A[0][23]
B0 | A[0][24] | A[0][25] | A[0][26] | A[0][27] | A[0][28] | A[0][29] | A[0][30] | A[0][31]
…
Notes: For Loop B to run without any cache misses other than compulsory misses, the data
cache needs to have the capacity to hold one column of matrix A. Since the consecutive
accesses in Loop B will use every eighth cache line and we have 128 elements in a matrix
A column, Loop B requires 128×8 or 1024 cache lines.

## Slide 8: A1.2: DM Cache
Consecutive accesses in Loop B use every 8th cache block (B0, B8, B16…), and we have 128 elements in a matrix A column, Loop B requires 128*8=1024 cache blocks to run with only compulsory misses.
  1st iteration accesses B0 (containing A[0][0]), B8 (containing A[1][0]), B16 (containing A[2][0]) … B1016 (containing A[127][0]).
  2nd iteration accesses B0 (containing A[0][1]), B8 (containing A[1][1]), B16 (containing A[2][1]) … B1016 (containing A[127][1]), all hits
  8th iteration accesses B1 (containing A[0][8]), B9 (containing A[1][8]), B17 (containing A[2][8]) … B1017 (containing A[127][8]).
  63th iteration accesses B7 (containing A[0][63]), B8 (containing A[1][63]), B16 (containing A[2][63]) … B1023 (containing A[127][63]).
But is 128 blocks sufficient?
  With 1024 blocks: first 8 iterations, use {B0, B8, B16…}; second 8 iterations, use {B1, B9, B17…}; next 8 iterations, use {B2, B10, B18…}.
  With 128 blocks: first 8 iterations, use {B0, B8, B16…}; second 8 iterations, use {B0, B8, B16…}; next 8 iterations, use {B0, B8, B16…}.
B0 | A[0][0] | A[0][1] | A[0][2] | A[0][3] | A[0][4] | A[0][5] | A[0][6] | A[0][7]
B1 | A[0][8] | A[0][9] | A[0][10] | A[0][11] | A[0][12] | A[0][13] | A[0][15] | A[0][15]
B2 | A[0][16] | A[0][17] | A[0][18] | A[0][19] | A[0][20] | A[0][21] | A[0][22] | A[0][23]
B3 | A[0][24] | A[0][25] | A[0][26] | A[0][27] | A[0][28] | A[0][29] | A[0][30] | A[0][31]
B4 | A[0][32] | A[0][33] | A[0][34] | A[0][35] | A[0][36] | A[0][37] | A[0][38] | A[0][39]
B5 | A[0][40] | A[0][41] | A[0][42] | A[0][43] | A[0][44] | A[0][45] | A[0][46] | A[0][47]
B6 | A[0][48] | A[0][49] | A[0][50] | A[0][51] | A[0][52] | A[0][53] | A[0][54] | A[0][55]
B7 | A[0][56] | A[0][57] | A[0][58] | A[0][59] | A[0][60] | A[0][61] | A[0][62] | A[0][63]
B8 | A[1][0] | A[1][1] | A[1][2] | A[1][3] | A[1][4] | A[1][5] | A[1][6] | A[1][7]
Loop A | Loop B
sum = 0; for (i = 0; i < 128; i++) for (j = 0; j < 64; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 64; j++) for (i = 0; i < 128; i++) sum += A[i][j];
…
Notes: For Loop B to run without any cache misses other than compulsory misses, the data
cache needs to have the capacity to hold one column of matrix A. Since the consecutive
accesses in Loop B will use every eighth cache line and we have 128 elements in a matrix
A column, Loop B requires 128×8 or 1024 cache lines.