## Slide 1: L10 Cache Optimizations
Zonghua Gu, 2018
5/4/2018
Acknowledgement: some slides taken from UC Berkeley CS61C

## Slide 2: Optimizations for the Memory Hierarchy
Write code that has locality!
  Spatial: access data contiguously
  Temporal: make sure access to the same data is not too far apart in time
How can you achieve locality?
  Adjust memory accesses in code (software) to improve miss rate (MR)
    Requires knowledge of both how caches work as well as your system’s parameters
  Proper choice of algorithm
  Loop transformations

## Slide 3: Example: Matrix Sum
Consider the following two loops, which calculate the sum of the entries in a 3x4 matrix A of 32-bit integers:
Loop A | Loop B
sum = 0; for (i = 0; i < 3; i++) for (j = 0; j < 4; j++) sum += A[i][j]; | sum = 0; for (j = 0; j < 4; j++) for (i = 0; i < 3; i++) sum += A[i][j];
Matrix A is stored contiguously in memory in row-major order. Row major order means that elements in the same row of the matrix are adjacent in memory (A[i][j] resides in memory location [4*(64*i + j)]).
Note: 76 is just one possible starting address of A
76
92
108
Layout in Memory
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]

## Slide 4: Matrix Sum Loop A
Index j is incremented in the inner loop
Good spatial locality for a[][]
No temporal locality for a[][]
  Each element is used only once
Access Pattern:
stride = 1
Layout in Memory
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
1) | a[0][0]
2) | a[0][1]
3) | a[0][2]
4) | a[0][3]
5) | a[1][0]
6) | a[1][1]
7) | a[1][2]
8) | a[1][3]
9) | a[2][0]
10) | a[2][1]
11) | a[2][2]
12) | a[2][3]
i
j
Loop A
sum = 0; for (i = 0; i < 3; i++) for (j = 0; j < 4; j++) sum += A[i][j];

## Slide 5: Matrix Sum Loop B
Layout in Memory
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
Access Pattern:
stride = 4
1) | a[0][0]
2) | a[1][0]
3) | a[2][0]
4) | a[0][1]
5) | a[1][1]
6) | a[2][1]
7) | a[0][2]
8) | a[1][2]
9) | a[2][2]
10) | a[0][3]
11) | a[1][3]
12) | a[2][3]
Index i is incremented in the inner loop
Poor spatial locality for a[][]
No temporal locality for a[][]
  Each element is used only once
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
i
j
Loop B
sum = 0; for (j = 0; j < 4; j++) for (i = 0; i < 3; i++) sum += A[i][j];

## Slide 6: Example: Matrix Multiplication
C
=
×
A
B
ai*
b*j
cij
The mathematical cache miss analysis in this example will not be covered in the exam. You only need to grasp the basic concept of cache blocking.
Notes: Subscript indices given in (row,col).

## Slide 7: Naïve Matrix Multiply
# move along rows of A
for (i = 0; i < n; i++)
# move along columns of B
for (j = 0; j < n; j++)
# EACH k loop reads row of A, col of B
# Also read & write c(i,j) n times
for (k = 0; k < n; k++)
C[i][j] += A[i][k] * B[k][j];
//Equivalent form
//C[i*n+j] += A[i*n+k] * B[k*n+j];
C(i,j)
A(i,:)
B(:,j)
C(i,j)
Notes: Note the += leads to an additional read of matrix C
Read A
Read B
Read C
Write C (guaranteed hit due to read of C)

## Slide 8: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  FA (Fully Associative) LRU cache, block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
Ignoring
matrix c
Each cache block holds 8 elements
Reading one row of Matrix A
  good spatial locality with stride 1
  1 cache miss every 8 elements; total cache misses due to reading one row of A is n/8
Reading one column of Matrix B
  poor spatial locality with stride n
  1 cache miss every element; total cache misses due to reading one column of B is n
Notes: Each cache block holds 8 matrix elements
A has good spatial locality
Stride 1
B has poor spatial locality
Stride n
By the time element n+1 is accessed, block has been kicked out of $
Iteration:
A = n/8
B = n

## Slide 9
1st cache miss brings 8 elements A[0][0], A[0][1] … A[0][7] into cache
2nd cache miss brings 8 elements B[0][0], B[0][1]… B[0][7] into cache
Compute A[0][0]*B[0][0]; Only B[0][0] is used
3rd cache miss brings 8 elements B[1][0], B[1][1] … B[1][7] into cache
Compute A[0][1]*B[1][0]
Only B[1][0] is used
4th cache miss brings 8 elements B[2][0], B[2][1] … B[2][7] into cache
Compute A[0][2]*B[2][0]
Only B[2][0] is used
9th cache miss brings 8 elements A[0][8], A[0][9] … A[0][15] into cache
10th cache miss brings 8 elements B[8][0], B[8][1] … B[8][7] into cache
Compute A[0][8]*B[8][0]
…
Notes: (n+1)th cache miss brings 8 elements B[n-1][0], B[n-1][1] … B[n-1][7] into cache
Compute A[1][0]*B[0][0] (by the time B

## Slide 10
At the end of multiplying 0th row of A[0][0…n-1] with 0th column of B[0…n-1][0], this is what the cache contains (assuming cache is quite small compared to matrix size)
By the time we get to 1st row of A[1][0…n-1], the top left elements of B have been evicted from the cache, so every element of B has to be fetched again from memory, even though they have been used before. So the process repeats.

## Slide 11: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
Total misses:
Ignoring
matrix c
n iterations of the doubly-nested loop

## Slide 12: Cache Blocking (1)
Can get the same result of a matrix multiplication by splitting the matrices into smaller submatrices (matrix “blocks”)
For example, multiply two 4×4 matrices:

## Slide 13: Cache Blocking (2)
Matrices of size , split into 4 blocks of size (=)
C22 = A21B12 + A22B22 + A23B32 + A24B42 = k A2k*Bk2
Multiplication operates on small “block” matrices
  Choose size so that they fit in the cache!
  This technique called “blocking”
C11
C12
C13
C14
C21
C22
C23
C24
C31
C32
C43
C34
C41
C42
C43
C44
A11
A12
A13
A14
A21
A22
A23
A24
A31
A32
A33
A34
A41
A42
A43
A144
B11
B12
B13
B14
B21
B22
B23
B24
B32
B32
B33
B34
B41
B42
B43
B44

## Slide 14: Blocked Matrix Multiply
Blocked version of the naïve algorithm:
  = block matrix size (assume divides evenly)
# move by rxr BLOCKS now
for (i = 0; i < n; i += r)
for (j = 0; j < n; j += r)
for (k = 0; k < n; k += r)
# block matrix multiplication
for (ib = i; ib < i+r; ib++)
for (jb = j; jb < j+r; jb++)
for (kb = k; kb < k+r; kb++)
c[ib][jb] += a[ib][kb]*b[kb][jb];
//Equivalently
//c[ib*n+jb] += a[ib*n+kb]*b[kb*n+jb];
Notes: 6 nested loops seems inefficient, but leads to faster code!
Outer three loops: loop over block matrices
Inner three loops: loop within block matrices

## Slide 15: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  At least two blocks () fit into cache: ; is multiple of 8
Each block iteration:
  misses per block
Total misses:
/ blocks
elements per block, 8 misses per cache block for each block of A or B
/ blocks in row and column
Ignoring
matrix c
Q: why r=1 is not a special case of the naïve approach?
A: r=1 does not satisfy condition “ is multiple of 8”
Notes: 3r2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm 𝑖𝑠 𝑚𝑢𝑙𝑡𝑖𝑝𝑙𝑒 𝑜𝑓 8

## Slide 16: Detailed Cache Miss Analysis (Blocked)
Consider one small block of C. We first multiply one block of A with one block of B, cache misses:
Repeat this for all n/r blocks of A (the top most “thick row”, and all n/r blocks of B (the leftmost “thick column”), # cache misses for computing the top left block of C is:
You need to do this for all (n/r)2 blocks of C in order to compute the big matrix C, so total # cache misses is:
/ blocks

## Slide 17
After finishing 1st block matrix multiply: misses for A, and misses for B
After finishing 2nd block matrix multiply: misses for B
After finishing nth block matrix: misses for A, misses for B, with total of misses.
Process repeats for times
Total misses:
Cache Miss Analysis (Blocked)

## Slide 18: Cache-Friendly Code
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache-friendly code”
  Getting absolute optimum performance is very platform specific
    Cache size, cache block size, associativity, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)
    Focus on inner loop code
Notes: Generic Code -> good rules of thumb

## Slide 19: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Notes: Increase stride size = less spatial locality = drop in throughput
Increase working set size = less temporal locality = fall out of respective caches
All caches on-chip