## Slide 1: L9 Cache II Exercises
5/7/2018
Acknowledgement: some slides taken from UC Berkeley CS61C

## Slide 2: Cache Replacement Policies
Consider 12-bit memory address. Consider two cache configurations: a DM cache with total size 128 Bytes, 16 Bytes/block (8 blocks); and a 4-way SA cache of the same size. For the SA cache, we consider two replacement policies – Least Recently Used (LRU) and First-In-First-Out (FIFO).
Consider the following sequence of memory addresses in hex, starting with an empty cache. Complete the following tables for the DM cache and both types of 4-way SA caches showing the progression of cache contents as accesses occur (in the tables, ‘inv’ = invalid, and the column of a particular cache block contains the tag of that block). You only need to fill in elements in the table when a value changes. The first few rows have been filled in for you.
Note that the table format is different from that in “L8 Cache I Exercises”, since we need to add a time dimension vertically.
  We use L0 to denote Cache Line 0, which means the same as Cache Block 0, to avoid confusion with B0 in “L8 Cache I Exercises”, which stands for Byte address 0 within a cache block.
  Each table entry contains Tag of that cache block, instead of cache content in “L8 Cache I Exercises”. For brevity, the hex prefix “0x” is omitted from the Tag.
Notes: , with distribution of Tag:Set Index:Offset bits as 5:3:4

## Slide 3: Tag:Set Index:Offset
For DM cache
  # Bytes/block=16  Offset is 4b
  # Sets=#blocks=128/16=8  SI is 3b
  Tag size=12-4-3=5
  Tag:Set Index:Offset bits: 5:3:4
For 4-way SA cache
  # Bytes/block=16  Offset is 4b
  # Sets=#blocks/#ways=(128/16)/4=2  SI is 1b
  Tag size=12-4-1=7
  Tag:Set Index:Offset bits: 7:1:4

## Slide 4: Q: DM Cache
Tag:Set Index:Offset bits: 5:3:4.
Memory address 0x110=000100010000(bin). Set Index=001(bin), hence it is mapped to L1, with Tag=10(bin)=0x2. Cache miss.
Memory address 0x136=000100110110(bin). Set Index=011(bin), hence it is mapped to L3, with Tag=10(bin)=0x2. Cache miss.
Memory address 0x202=001000000010(bin). Set Index=000(bin), hence it is mapped to L0, with Tag=100(bin)=0x4. Cache miss.
Address | DM Cache |  |  |  |  |  |  |  | 
 | Cache Block (Tag in Hex) |  |  |  |  |  |  |  | hit?
 | L0 | L1 | L2 | L3 | L4 | L5 | L6 | L7 | 
0x110 | inv | 2 | inv | inv | inv | inv | inv | inv | N
0x136 |  |  |  | 2 |  |  |  |  | N
0x202 | 4 |  |  |  |  |  |  |  | N
0x1A3 |  |  |  |  |  |  |  |  | 
0x102 |  |  |  |  |  |  |  |  | 
0x361 |  |  |  |  |  |  |  |  | 
0x204 |  |  |  |  |  |  |  |  | 
0x114 |  |  |  |  |  |  |  |  | 
0x1A4 |  |  |  |  |  |  |  |  | 
0x177 |  |  |  |  |  |  |  |  | 
0x301 |  |  |  |  |  |  |  |  | 
0x206 |  |  |  |  |  |  |  |  | 
0x135 |  |  |  |  |  |  |  |  | 
Time

## Slide 5: A: DM Cache
Memory address 0x110=000100010000(bin). Set Index=001(bin), hence it is mapped to L1, with Tag=10(bin)=0x2. Cache miss.
Memory address 0x136=000100110110(bin). Set Index=011(bin), hence it is mapped to L3, with Tag=10(bin)=0x2. Cache miss.
Memory address 0x202=001000000010(bin). Set Index=000(bin), hence it is mapped to L0, with Tag=100(bin)=0x4. Cache miss.
Memory address 0x114=000100010100(bin). Set Index=001(bin), hence it is mapped to L1, with Tag=10 (bin)=0x2. Cache hit!
  Memory addresses 0x110 and 0x114 only differ in their offsets, hence they are in the same cache block (with size 16 Bytes). Access to 0x110 was a miss, and brought in the cache block, so access to 0x114 is a hit.
Memory address 0x1A4=000110100100(bin). Set Index=010(bin), hence it is mapped to L2, with Tag=11 (bin)=0x3. Cache hit!
Memory address 0x135=000100110101(bin). Set Index=011(bin), hence it is mapped to L3, with Tag=10 (bin)=0x2. Cache hit!
Address | DM Cache |  |  |  |  |  |  |  | 
 | Cache Block (Tag in Hex) |  |  |  |  |  |  |  | hit?
 | L0 | L1 | L2 | L3 | L4 | L5 | L6 | L7 | 
0x110 | inv | 2 | inv | inv | inv | inv | inv | inv | N
0x136 |  |  |  | 2 |  |  |  |  | N
0x202 | 4 |  |  |  |  |  |  |  | N
0x1A3 |  |  | 3 |  |  |  |  |  | N
0x102 | 2 |  |  |  |  |  |  |  | N
0x361 |  |  |  |  |  |  | 6 |  | N
0x204 | 4 |  |  |  |  |  |  |  | N
0x114 |  | 2 |  |  |  |  |  |  | Y
0x1A4 |  |  | 3 |  |  |  |  |  | Y
0x177 |  |  |  |  |  |  |  | 2 | N
0x301 | 6 |  |  |  |  |  |  |  | N
0x206 | 4 |  |  |  |  |  |  |  | N
0x135 |  |  |  | 2 |  |  |  |  | Y
3 cache hits, 10 misses

## Slide 6: Q: 4-Way SA Cache w/ LRU
Address | 4-Way SA Cache |  |  |  |  |  |  |  | 
 | Cache Block (Tag in Hex) |  |  |  |  |  |  |  | hit?
 | Set 0 |  |  |  | Set 1 |  |  |  | 
 | Way0 | Way1 | Way2 | Way3 | Way0 | Way1 | Way2 | Way3 | 
0x110 | Inv | Inv | Inv | Inv | 08 | Inv | Inv | inv | N
0x136 |  |  |  |  |  | 09 |  |  | N
0x202 | 10 |  |  |  |  |  |  |  | N
0x1A3 |  |  |  |  |  |  |  |  | 
0x102 |  |  |  |  |  |  |  |  | 
0x361 |  |  |  |  |  |  |  |  | 
0x204 |  |  |  |  |  |  |  |  | 
0x114 |  |  |  |  |  |  |  |  | 
0x1A4 |  |  |  |  |  |  |  |  | 
0x177 |  |  |  |  |  |  |  |  | 
0x301 |  |  |  |  |  |  |  |  | 
0x206 |  |  |  |  |  |  |  |  | 
0x135 |  |  |  |  |  |  |  |  | 
Tag:Set Index:Offset bits: 7:1:4.
Memory address 0x110=000100010000(bin). Set Index=1(bin), hence it is mapped to Set 1, with Tag=1000(bin)=0x8. It can be placed anywhere in the 4 ways of Set 1, but let’s assume it is placed in Way 0. Cache miss.
Memory address 0x136=000100110110(bin). Set Index=1(bin), hence it is mapped to Set 1, with Tag=1001(bin)=0x9. It can be placed anywhere in the remaining 3 ways of Set 1, but let’s assume it is placed in Way 1. Cache miss.
Memory address 0x202=001000000010(bin). Set Index=0(bin), hence it is mapped to Set 0, with Tag=10000(bin)=0x10. It can be placed anywhere in the 4 ways of Set 0, but let’s assume it is placed in Way 0. Cache miss.

## Slide 7: A: 4-Way SA Cache w/ LRU
4-way Address | LRU Cache |  |  |  |  |  |  |  | 
 | Cache Block (Tag in Hex) |  |  |  |  |  |  |  | hit?
 | Set 0 |  |  |  | Set 1 |  |  |  | 
 | Way0 | Way1 | Way2 | Way3 | Way0 | Way1 | Way2 | Way3 | 
0x110 | Inv | Inv | Inv | Inv | 08 | Inv | Inv | inv | N
0x136 |  |  |  |  |  | 09 |  |  | N
0x202 | 10 |  |  |  |  |  |  |  | N
0x1A3 |  | 0D |  |  |  |  |  |  | N
0x102 |  |  | 08 |  |  |  |  |  | N
0x361 |  |  |  | 1B |  |  |  |  | N
0x204 | 10 |  |  |  |  |  |  |  | Y
0x114 |  |  |  |  | 08 |  |  |  | Y
0x1A4 |  | 0D |  |  |  |  |  |  | Y
0x177 |  |  |  |  |  |  | 0B |  | N
0x301 |  |  | 18 |  |  |  |  |  | N
0x206 | 10 |  |  |  |  |  |  |  | Y
0x135 |  |  |  |  |  | 09 |  |  | Y
4-Way SA cache with 8 blocks, has 2 sets, and distribution of Tag:Set Index:Offset bits as 7:1:4.
Memory address 0x110=000100010000(bin). Set Index=1(bin), hence it is mapped to Set 1, with Tag=1000(bin)=0x08. No tag match, cache miss. It can be placed anywhere in the 4 ways of Set 1, but let’s assume it is placed in Way 0.
Memory address 0x136=000100110110(bin). Set Index=1(bin), hence it is mapped to Set 1, with Tag=1001(bin)=0x09. No tag match, cache miss. It can be placed anywhere in the remaining 3 ways of Set 1, but let’s assume it is placed in Way 1.
Memory address 0x202=001000000010(bin). Set Index=0(bin), hence it is mapped to Set 0, with Tag=10000(bin)=0x10. No tag match, cache miss. It can be placed anywhere in the 4 ways of Set 0, but let’s assume it is placed in Way 0.
Memory address 0x204=001000000100(bin). Set Index=0(bin), hence it is mapped to Set 0, with Tag=10000(bin)=0x10. Tag match with block in Way 0, cache hit!
Memory address 0x177=000101110111(bin). Set Index=1(bin), hence it is mapped to Set 1, with Tag=1011(bin)=0x0B. No tag match, cache miss. It can be placed anywhere in the remaining 2 ways of Set 1, but let’s assume it is placed in Way 2.
Memory address 0x301=001100000001(bin). Set Index=0(bin), hence it is mapped to Set 0, with Tag=11000(bin)=0x18. No tag match, cache miss. It replaces the LRU block in Way 2.
5 cache hits, 8 misses

## Slide 8: Q: 4-Way SA Cache w/ FIFO
4-way Address | FIFO Cache |  |  |  |  |  |  |  | 
 | Cache Block (Tag in Hex) |  |  |  |  |  |  |  | hit?
 | Set 0 |  |  |  | Set 1 |  |  |  | 
 | Way0 | Way1 | Way2 | Way3 | Way0 | Way1 | Way2 | Way3 | 
0x110 | Inv | Inv | Inv | Inv | 08 | Inv | Inv | inv | N
0x136 |  |  |  |  |  | 09 |  |  | N
0x202 | 10 |  |  |  |  |  |  |  | N
0x1A3 |  |  |  |  |  |  |  |  | 
0x102 |  |  |  |  |  |  |  |  | 
0x361 |  |  |  |  |  |  |  |  | 
0x204 |  |  |  |  |  |  |  |  | 
0x114 |  |  |  |  |  |  |  |  | 
0x1A4 |  |  |  |  |  |  |  |  | 
0x177 |  |  |  |  |  |  |  |  | 
0x301 |  |  |  |  |  |  |  |  | 
0x206 |  |  |  |  |  |  |  |  | 
0x135 |  |  |  |  |  |  |  |  | 
4-Way SA cache with 8 blocks, has 2 sets, and distribution of Tag:Set Index:Offset bits as 7:1:4.
Memory address 0x110=000100010000(bin). Set Index=1(bin), hence it is mapped to Set 1, with Tag=1000(bin)=0x8. It can be placed anywhere in the 4 ways of Set 1, but let’s assume it is placed in Way 0. Cache miss.
Memory address 0x136=000100110110(bin). Set Index=1(bin), hence it is mapped to Set 1, with Tag=1001(bin)=0x9. It can be placed anywhere in the remaining 3 ways of Set 1, but let’s assume it is placed in Way 1. Cache miss.
Memory address 0x202=001000000010(bin). Set Index=0(bin), hence it is mapped to Set 0, with Tag=10000(bin)=0x10. It can be placed anywhere in the 4 ways of Set 0, but let’s assume it is placed in Way 0. Cache miss.

## Slide 9: A: 4-Way SA Cache w/ FIFO
4-way Address | FIFO Cache |  |  |  |  |  |  |  | 
 | Cache Block (Tag in Hex) |  |  |  |  |  |  |  | hit?
 | Set 0 |  |  |  | Set 1 |  |  |  | 
 | Way0 | Way1 | Way2 | Way3 | Way0 | Way1 | Way2 | Way3 | 
0x110 | Inv | Inv | Inv | Inv | 08 | Inv | Inv | inv | N
0x136 |  |  |  |  |  | 09 |  |  | N
0x202 | 10 |  |  |  |  |  |  |  | N
0x1A3 |  | 0D |  |  |  |  |  |  | N
0x102 |  |  | 08 |  |  |  |  |  | N
0x361 |  |  |  | 1B |  |  |  |  | N
0x204 | 10 |  |  |  |  |  |  |  | Y
0x114 |  |  |  |  | 08 |  |  |  | Y
0x1A4 |  | 0D |  |  |  |  |  |  | Y
0x177 |  |  |  |  |  |  | 0B |  | N
0x301 | 18 |  |  |  |  |  |  |  | N
0x206 |  | 10 |  |  |  |  |  |  | N
0x135 |  |  |  |  |  | 09 |  |  | Y
4-Way SA cache with 8 blocks, has 2 sets, and distribution of Tag:Set Index:Offset bits as 7:1:4.
Memory address 0x301=001100000001(bin). Set Index=0(bin), hence it is mapped to Set 0, with Tag=11000(bin)=0x18. No tag match, cache miss. It replaces the block in Way 2, which entered the cache the earliest (by access to 0x202).
Memory address 0x206=001000000110(bin). Set Index=0(bin), hence it is mapped to Set 0, with Tag=10000(bin)=0x10. No tag match, cache miss. It replaces the block in Way 1, which entered the cache the earliest (by access to 0x1A3).
4 cache hits, 9 misses

## Slide 10: Q: AMAT
Assume that the results of the above analysis can represent the average miss-rates. What would be the average memory access latency in CPU cycles for each type of cache? Assuming:
  Cache hit time is 2 cycles for DM cache, 3 cycles for 4-way SA cache
  Cache miss penalty is 20 cycles for both

## Slide 11: A: AMAT
The miss rate for the DM cache is 10/13. The miss rate for the LRU 4-way SA cache is 8/13. The miss rate for the FIFO 4-way SA cache is 9/13.
  For DM cache, AMAT = 2+(10/13)*20 = 17.38 ≈ 18 cycles.
  For LRU 4-way SA cache, AMAT = 3 + (8/13)*20 = 15.31 ≈ 16 cycles.
  For FIFO 4-way SA cache, AMAT = 3 + (9/13)*20 = 16.85 ≈ 17 cycles.
LRU 4-way SA cache has the best performance in terms of AMAT

## Slide 12: LRU vs. FIFO
Q: Does LRU always outperform FIFO?
A: No. Neither is optimal.
Consider an FA cache with 2 blocks, and an access sequence for memory addresses in blocks 1, 2, 1, 3, 2.
With LRU: 1 (M), 2(M), 1(H), 3(M, replaces block 2), 2(M)
With FIFO: 1 (M), 2(M), 1(H), 3(M, replaces block 1), 2(H)
LRU1 hit; FIFO2 hits
Consider an FA cache with 2 blocks, and an access sequence for memory addresses in blocks 1, 2, 1, 3, 1.
With LRU: 1 (M), 2(M), 1(H), 3(M, replaces block 2), 1(H)
With FIFO: 1 (M), 2(M), 1(H), 3(M, replaces block 1), 1(M)
LRU2 hits; FIFO1 hit

## Slide 13: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average time to access memory considering both hits and misses in the cache
  AMAT = Hit rate * Hit time + Miss rate * Miss time
  = (1 – Miss rate)*Hit time + Miss rate * (Hit time + Miss penalty)
  = Hit time + Miss rate * Miss penalty
5/7/2018
Review
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 14: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  L2 Local Miss Rate = L2 Misses / L1 Misses
Global miss rate – the fraction of references that miss in all levels of caches and must go to memory
    Global Miss rate = L2 Misses / Total Accesses
    = (L2 Misses / L1 Misses) × (L1 Misses / Total Accesses)
    = L2 Local Miss Rate × L1 Local Miss Rate
  L1 Miss Penalty = L2 AMAT; L2 Miss Penalty = Memory access time
  L1 cache only: AMAT = Hit Time + Miss rate × Miss penalty
  L1+L2 caches: AMAT = L1 Hit Time + L1 Local Miss rate × (L2 Hit Time + L2 Local Miss rate × L2 Miss penalty)
5/7/2018
Review

## Slide 15: Question: AMAT
Compute AMAT for 1-level cache system, given:
  L1 Hit Time: 1 cycle, L1 Miss Rate: 2%
  Main Memory access time: 51 cycles
  CPU clock cycle time: 200 ps/cycle
Which of the following results in largest decrease in AMAT?
  Faster CPU with 190 ps cycle time
  Reduce miss penalty to 40 clock cycles
  Reduce miss rate to 0.015 misses/instruction
Notes: Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
  AMAT = HT + MR*MP =

## Slide 16: Answer: AMAT
Compute AMAT for 1-level cache system, given:
  L1 Hit Time: 1 cycle, L1 Miss Rate: 2%
  Main Memory access time: 51 cycles
  CPU clock cycle time: 200 ps/cycle
A: Miss penalty = 50 cycles; AMAT = 1 +.02*50 = 2 cycles = 400 ps
Which of the following results in largest decrease in AMAT?
  Faster CPU with 190 ps cycle time
    AMAT = 1 +.02*50 = 2 cycles = 380 ps
  Reduce miss penalty to 40 clock cycles
    AMAT = 1 +.02*40 = 1.8 cycles = 360 ps
  Reduce miss rate to 0.015 misses/instruction
    AMAT = 1 +.015*50 = 1.75 cycles = 350 ps
Notes: Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
  AMAT = HT + MR*MP =

## Slide 17: Question: AMAT
For 2-level cache system, given:
  For every 1000 instructions, on average
    40 misses in L1, 20 misses in L2
  L1 Hit Time: 1 cycle
  L2 Hit Time: 10 cycles
  Main memory access time: 100 cycles
Compute local miss rate, AMAT, stall cycles per instruction

## Slide 18: Answer: AMAT
For 2-level cache system, given:
  For every 1000 instructions, on average
    40 misses in L1, 20 misses in L2
  L1 Hit Time: 1 cycle
  L2 Hit Time: 10 cycles
  Main memory access time: 100 cycles
Compute:
  1. L1 local miss rate, L2 local miss rate, global miss rate; AMAT
  2. Repeat for the case without L2 cache
A: 1. With L2 cache: L1 local miss rate=40/1000=0.04; L2 local miss rate = 20/40 = 0.5; global miss rate = 20/1000 = 0.02; AMAT=1+0.04*(10+0.5*100)=3.4
2. If we remove the L2 cache: L1 local miss rate=0.04; AMAT=1+0.04*100=5

## Slide 19: Question: AMAT
Compute AMAT for 2-level cache system, given:
  L1 Hit Time: 1 cycle, L1 Local Miss Rate: 3%
  L2 Hit Time: 6 cycle, L2 Local Miss Rate: 10%.
  Main Memory access time: 120 cycles

## Slide 20: Answer: AMAT
Compute AMAT for 2-level cache system, given:
  L1 Hit Time: 1 cycle, L1 Local Miss Rate: 3%
  L2 Hit Time: 6 cycle, L2 Local Miss Rate: 10%.
  Main Memory access time: 120 cycles
AMAT = 1 + .03*(6 + .10*120) = 1.54

## Slide 21: Question: AMAT
Assuming main memory access time is 100 cycles. Compute AMAT for
1. 16KB L1 cache only with hit time 2 cycles, and hit rate 90%
2. 128KB L1 cache only with hit time 10 cycles, and hit rate 97.5%
3. 16KB L1 cache + 128KB L2 cache
  L1 Hit Time: 2 cycles, Local Hit Rate: 90%
  L2 Hit Time: 12 cycles, Local Hit Rate: 75%

## Slide 22: Answer: AMAT
Assuming main memory access time is 100 cycles. Compute AMAT for
1. 16KB L1 cache only with hit time 2 cycles, and hit rate 90%
  A: 2+0.1*100=12 cycles
2. 128KB L1 cache only with hit time 10 cycles, and hit rate 97.5%
  A: 10+0.025*100=12.5 cycles
3. 16KB L1 cache + 128KB L2 cache
  L1 Hit Time: 2 cycles, Local Hit Rate: 90%
  L2 Hit Time: 12 cycles, Local Hit Rate: 75%
  A: 2+0.1*(10+0.25*100)=5.5 cycles