## Slide 1: CSC 112: Computer Operating Systems Lecture XX I/O
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on UC Berkeley CS 162: Operating Systems and System Programming

## Slide 2: Outlines
I/O devices
I/O hardware
I/O communication protocol
I/O communication methods
Hard Disk Drives (HDDs)
Solid-state Disks (SSDs)

## Slide 3: I/O Devices
I/O and computing are two components of a computer
  I/O is an important part of computing systems
I/O devices
  HW can easily let us plug in diverse devices
  OS can efficiently manage and interact with different devices
Two trends:
  Standardization of software and hardware interfaces
  New types of I/O devices
Diversity of I/O devices
  Storage: Disks, SSDs
  Transmission: Network connections, Bluetooth
  Human computer interface: Screen, keyboard, mouse, mic, speaker
Notes: Three‑axis gyro. Gyroscope sensor
Accelerometer.
Proximity sensor.
Ambient light sensor

## Slide 4: I/O Hardware
A hierarchical structure
Memory bus:
  60GB/sec
PCI bus:
  8-10GB/sec
Peripheral I/O bus
  100-500MB/sec

## Slide 5: I/O Hardware in a Typical PC
Notes: Direct Media Interface proprietary DMI 4.0

## Slide 6: I/O Hardware
Port: Connection point for devices,
  USB, HDMI, DP
Bus: Shared direct access
  PCIe, expansion bus, SATA
Controller: electronics that operate port, bus, device
  Contains processor, microcode, private memory, bus controller
Device driver:
  Present uniform device-access interface to I/O subsystem
OS
Write
Read
Notes: Peripheral Component Interconnect

## Slide 7: I/O Communication Protocol
CPU:
DISK:
A
SPIN for A
B
Busy
A
CPU:
DISK:
A
B
Busy
A
B
Request
& Sleep
Context
Switch
Interrupt
Interrupts allow for overlap of computation and I/O
A
A
Polling
(Busy-waiting)
Interrupt
(Sleep while waiting)
Notes: interrupt service routine

## Slide 8: Interrupts VS. Polling
Fast device: Better to spin-wait than take interrupt overhead
Flood of interrupts arrive
  Can lead to livelock (always handling interrupts)
Performance improvement
  Interrupt coalescing (batch together several interrupts)
Notes: Device time unknown? Hybrid approach (spin then use interrupts)
Better to ignore interrupts while make some progress handling them

## Slide 9: Programmed I/O (PIO)
Programmed I/O
  CPU directly tells device what the data is
Data transfer can be still costly
CPU:
DISK:
A
B
A
A
DATA

## Slide 10: Direct Memory Access (DMA)
Used to avoid PIO for large data movement
Bypasses CPU to transfer data directly between I/O device and memory
DMA controller
CPU:
DISK:
A
B
A
A
DATA
DMA:
Notes: A simple DMA controller is a standard component in all modern computers, from smartphones to mainframes

## Slide 11: Direct Memory Access (DMA)

## Slide 12: I/O Communication Methods
I/O instructions
  Each device has a port
  IN/OUT instructions (x86) communicate with device
    IN Reg port
    OUT Reg port
Memory-Mapped I/O
  H/W maps registers into address space
  Loads/stores sent to device

## Slide 13: Device Drivers
Devices are diverse
Each has its own protocols
Abstraction – Device Drivers
  Hide the details and differences
  Provide standard interfaces
Notes: They either design new devices to be compatible with an existing host controller interface (such as SATA), or they write device drivers to interface the new hardware to popular operating systems.

## Slide 14: Hard Disk Drives (HDDs)
A magnetic disk has a sector-addressable address space
  A disk as an array of sectors
  Each sector (logical block) is the smallest unit of transfer
Sectors are typically 512 or 4096 bytes
Main operations
  Read from sectors (blocks)
  Write to sectors (blocks)

## Slide 15: Hard Disk Drives (HDDs)
Outer tracks with more sectors
Inner tracks with fewer sectors
All tracks have the same number of sectors
OLD
New
Notes: Figure from Modern Operating Systems 5 ED

## Slide 16: Hard Disk Drives (HDDs)
Sectors
Tracks
Platter (sides)
Arm-head
Spindle
Rate of rotation: rotations per minute (RPM)
  7,200 – 15,000

## Slide 17: Hard Disk Drives (HDDs)
Seek for the right track
Rotate from 9 to 0
Transfer data from sector 0

## Slide 18: Hard Disk Drives (HDDs)
Seek time
Rotational delay
Transfer latency
The overall latency
At millisecond level

## Slide 19: Hard Disk Drives (HDDs)
Seek: may take several milliseconds (ms)
  Function of cylinder distance
  Entire seek often takes 4-10ms
Rotate: Depends on RPM
  7200 RPM is common, 15000 RPM is high end
  Old computers may have 5400 RPM disks
  1 min / 7200 RPM = 60 sec / 7200 RPM = 8.3 ms / rotation
  On average it may take 4.2 ms (*0.5)
Transfer: Depends on RPM and sector density
  Pretty fast
  100+ MB/s for SATA I (1.5Gb/s), up to 600MB/s for SATA III (6.0Gb/s)
  512-byte sector: 1s / 100 MB = 10ms /MB = 4.9 us/sector

## Slide 20: HDDs’ Performance
Metric | Perf
Avg Seek | 4ms
RPM | 7200
Max Transfer | 500MB/s
Read 4KB
Avg Seek
Avg Rotate

## Slide 21: Effect of Workloads
Seeks and rotations are slow while transfer is relatively fast
What kind of workload is best suited for disks?
  Sequential I/O: access sectors in order
  Most of time is spent on transferring
Random workloads access sectors in a random order
  Slow on disks
  Seek+rotation dominate
  Avoid random I/O if possible

## Slide 22: Solid-State Disk (SSD)
HDD – Mechanical Disk
  Slow (seek, rotate, transfer)
  Poor performance for random I/O
  $ cheap
  High capacity
Solid-state disk (SSD) – flash based disk
  Single or multiple transistors for storage
  Fast: no moving, no seek
  Parallel
  $$ More expensive
  Wear out issue

## Slide 23: SSD
HDD – Mechanical Disk
  Slow (seek, rotate, transfer)
  Poor performance for random I/O
  $ cheap
Solid-state disk (SSD) – flash based disk
  Single or multiple transistors for storage
  Fast: no moving, no seek
  Parallel
  $$ More expensive

## Slide 24: SSD
Single level cell (SLC)
0
1
charge
Multi-level cell (MLC)
00
01
10
11
charge
0

## Slide 25: SSD
 | SLC | MLC | TLC
Bit/Cell | 1 bit | 2 bit | 3 bit
Performance | High | Media | Low
Reliability | High | Media | Low
Capacity | Low | Media | High
Price | High | Media | Low
Applications | Servers, industrial applications | Consumer products | Most of consumer products
Quadruple level cell (QLC) is also available.

## Slide 26: SSD

## Slide 27: SSD
SSD
A NAND-flash memory is divided into banks
  Banks can be accessed in parallel
Each bank consists of many blocks
  Erase unit
  1024– 4096 blocks for a bank
  128 or 256 KB
Each block is made of pages
  Read & write unit
  4KB, 2-8KB
Block 0
Block 1
Block 2
Block 3
Page
Bank

## Slide 28: SSD
Writing to a page is strange and costly
  We cannot directly overwrite a used page
  We must erase the target page before writing
    Erase
    Program
101010
110011
111001
100111
page 0
page 1
page 2
page 3
Write 101100 to page 0
Block

## Slide 29: SSD
Block
Writing to a page is strange and costly
  We cannot directly overwrite a used page
  We must erase the target page before writing
    Erase
    Program
111111
110011
111001
100111
page 0
page 1
page 2
page 3
Erase page 0
Write 101100 to page 0

## Slide 30: SSD
Block
Writing to a page is strange and costly
  We cannot directly overwrite a used page
  We must erase the target page before writing
    Erase
    Program
101100
110011
111001
100111
page 0
page 1
page 2
page 3
Write 101100 to page 0
Erase page 0
Program 101100 to page 0

## Slide 31: SSD
Programming one page needs to erase the whole block
  Use memory to temporarily store blocks
101010
110011
111001
100111
page 0
page 1
page 2
page 3
Block 0
Write 101100 to page 0
Erase all pages
111111
111111
111111
111111
page 0
page 1
page 2
page 3
Block 0

## Slide 32: SSD
Programming one page needs to erase the whole block
101010
110011
111001
100111
page 0
page 1
page 2
page 3
Block 0
111111
111111
111111
111111
page 0
page 1
page 2
page 3
Block 0
Memory
SSD

## Slide 33: SSD
Programming one page needs to erase the whole block
101100
110011
111001
100111
page 0
page 1
page 2
page 3
Block 0
101100
110011
111001
100111
page 0
page 1
page 2
page 3
Block 0
Memory
SSD
Program page 0

## Slide 34: SSD
Latency of SSD
  Read: 10-50us
  Erase: 2ms
  Program: 200-500us
Wear-out
  Erasing and programming slowly accrue a little bit of extra charge.
  Difficult to distinguish 0 and 1 over time.
  Evenly distribute data over SSD to avoid overuse of some pages and banks
0
0
0
0
0

## Slide 35: Summary
I/O Devices
Standardized interface
Interrupt vs Polling
DMA vs PIO
The structure and performance of HDDs
The structure of SSDs