## Slide 1: CSC 112: Computer Operating Systems Lecture XX TODO
Department of Computer Science,
Hofstra University
Acknowledgement: Lecture slides based on UC Berkeley CS 162: Operating Systems and System Programming

## Slide 2
Real-Time Operating Systems M
9. Real-Time: Basic Concepts

## Slide 3: Notice
9.2
Torroni, Real-Time Operating Systems M ©2013
The course material includes slides downloaded from: http://codex.cs.yale.edu/avi/os-book/
(slides by Silberschatz, Galvin, and Gagne, associated with Operating System Concepts, 9th Edition, Wiley, 2013)
and
http://retis.sssup.it/~giorgio/rts-MECS.html
(slides by Buttazzo, associated with Hard Real-Time Computing
Systems, 3rd Edition, Springer, 2011)
which has been edited to suit the needs of this course. The slides are authorized for personal use only.
Any other use, redistribution, and any for profit sale of the slides (in any form) requires the consent of the copyright owners.

## Slide 4: Objectives
Study software methodologies to support time critical systems:
  Study software methodologies and algorithms to increase predictability
in (embedded) computing system…
…consisting of several concurrent activities…
…subject to timing constraints
  Learn how to model and analyze a real-time application to predict worst-case response times and verify its feasibility under a set of constraints

## Slide 5: Control and Implementation
Often, control and implementation are done by different people that do not talk to each other:
Control guys typically assume a computer with infinite resources and computational power. In some case, computation is modeled by a fixed delay Δ.

## Slide 6: Control and Implementation
In reality, a computer:
  has limited resources
  finite computational power (non null execution times)
  executes several concurrent activities
  introduces variable delays (often unpredictable)
Modeling such factors and taking them into account in the design phase allows a significant improvement in performance and reliability

## Slide 7
Definitions
and
Sample Applications

## Slide 8: Embedded System
Environment
actuators
sensors
micro- processor
A computing system hidden in an object to control its functions, enhance its performance, manage the available resources and simplify the interaction with the user.
Object
communication
user
other units

## Slide 9: Control System Components
In every control application, we can distinguish 3 basic components:
  The system to be controlled
    may include sensors and actuators
  The controller
    sends signals to the system according to a predetermined control objective
  The environment in which the system operates

## Slide 10: A Typical Control System
Other activities
  filtering, classification, data fusion, recognition, planning
System
Controller
actuators
Environ.
internal state
external state
feedback
sensor
sensor
Sensory processing
pre- processing

## Slide 11: Software Vision
computer
actuators
D/A
Environ.
sensors
A/D
Thread (task)
Resource

## Slide 12: Types of Control Systems
Depending on the system-environment interactions, we can distinguish among 3 types of control systems:
  Monitoring systems
    do not modify the environment
  Open-loop control systems
    loosely modify the environment
  Closed-loop control systems
    tight interaction between perception and action

## Slide 13: Monitoring Systems
Do not modify the environment
  surveillance systems, air traffic control
Environ- ment
Data processing
sensors
sensors
.
.
Real-time system
sensors
Display

## Slide 14: Open-Loop Control Systems
Sensing and control are loosely coupled
  Assembly robots, sorting robots
Environ- ment
System
Controller
actuators
sensors
Data processing
Planning

## Slide 15: Closed-Loop Control Systems
Sensing and control are tightly coupled
  Flight control systems, military systems, living beings
Environ- ment
System
Controller
actuators
sensors
Data processing
Planning

## Slide 16: Implications
The tight interaction with the environment requires the system to react to events within precise timing constraints
Timing constraints are imposed by the dynamics of the environment
The operating system must be able to execute tasks within timing constraints

## Slide 17: A Robot Control Example
Consider a robot equipped with:
  two actuated wheels
  two proximity (US) sensors
  a mobile (pan/tilt) camera
  a wireless transceiver
Goal:
  follow a path based on visual feedback
  avoid obstacles
  send complete robot status every 20 ms

## Slide 18: Hierarchical Control
visual−based navigation
visual tracking
obstacle avoidance
10 ms
100 ms
object recognition
mot_dx
mot_sx
pan
tilt
camera
US1 US2
1 ms
vehicle control
5 ms
20 ms
feature extraction
motor control
motor control
motor control
motor control
1 ms

## Slide 19: Design Requirements
Modularity: a subsystem must be developed without knowing the details of other subsystems (team work)
Configurability: software must be adapted to different situations (through the use of suitable parameters) without changing the source code
Portability: minimize code changes when porting the system to different hardware platforms
Predictability: allow the estimation of maximum delays
Efficiency: optimize the use of available resources (computation time, memory, energy)

## Slide 20: Operating System Requirements
Timeliness: results must be correct not only in their value but also in the time domain
  provide kernel mechanism for time management and for handling tasks with explicit timing constraints and different criticality
Predictability: system must be analyzable to predict the consequences of any scheduling decision
  if some task cannot be guaranteed within time constraints, system must notify this in advance, to handle the exception (plan alternative actions)
Efficiency: operating system should optimize the use of available resources (computation time, memory, energy)
Robustness: must be resilient to peak-load conditions
Fault tolerance: single software/hardware failures should not cause the system to crash
Maintainability: modular architecture to ensure that modifications are easy to perform

## Slide 21: Modularity
Modularity can be achieved by:
  partitioning the system into a set of subsystems, each managed by one or more computational tasks
  the definition of precise interfaces between tasks, each specifying:
    data exchanged with the other tasks (input and output)
    functionality of the task (what it has to do)
    validity assumptions (e.g., admissible ranges)
    performance requirements (priority, period, deadline, jitter)
Asynchronous communication mechanisms

## Slide 22: Control View
visual−based navigation
visual tracking
obstacle avoidance
10 ms
100 ms
object recognition
mot_dx
mot_sx
pan
tilt
camera
US1 US2
1 ms
vehicle control
5 ms
20 ms
feature extraction
motor control
motor control
motor control
motor control
1 ms

## Slide 23: Software View
periodic task
buffer
visual tracking
obstacle avoidance
vehicle control
visual−based navigation
object recognition
mot_dx
mot_sx
pan
tilt
camera
US1 US2
feature extraction
motor control

## Slide 24: RTOS Responsibilities
The Real-Time Operating System (RTOS) is responsible for:
  managing the concurrent execution of the various activities
    concurrent tasks
  decide the order of execution of the tasks, satisfying the specified requirements
    scheduling
  solving possible timing conflicts during the access of shared resources
    critical sections
  manage the timely execution of asynchronous events
    interrupts

## Slide 25: What is a Real-Time System?
A computer system able to respond to events within precise timing constraints
x (t)
RT system Environment
t
y (t+)
A system where the correctness depends not only on the output values, but also on the time at which results are produced

## Slide 26: Typical Objection
“It is not worth to invest in Real Time theory, because computer speed is increasing exponentially, and all timing constraints can eventually be handled.”
Answer
Given an arbitrary computer speed, we must always guarantee that timing constraints can be met. Testing is NOT sufficient

## Slide 27: Real-Time ≠ Fast
A real-time system is not a fast system
Speed is always relative to a specific environment
Running faster is good, but does not guarantee a correct behaviour.
The objective of a real-time system is to guarantee the timing behaviour of each individual task
The objective of a fast system is to minimize the average response time of a task set. But…
  Don’t trust average when you have to guarantee individual
performance

## Slide 28: Sources of Nondeterminism
Architecture
  cache, pipelining, interrupts, DMA
Operating System
  scheduling, synchronization, communication
Language
  lack of explicit support for time
Design Methodologies
  lack of analysis and verification techniques

## Slide 29: Design Methodologies
Traditional approach: empirical techniques
  assembly programming
  timing through dedicated timers
  control through driver programming
  priority manipulations
Many disadvantages!
  tedious programming, heavily relies on programmer’s ability
  difficult code understanding (readability × efficiency = k)
  difficult software maintainability
 MLOC, understanding takes more than rewriting => bug prone
  difficult to verify timing constraints without OS & language support

## Slide 30: Implications
Dangerous way of programming real-time applications
May work in most situations, but high risk of failure
When the system fails, it is very difficult to understand why
Low reliability
Many famous failures
  First flight of the Space Shuttle, 1979 (transient overload at initialization)
    probability of failure ~1.5%
  Scud missile on Dhahran, 1993 (delay due to interrupt handling)
    program flow depends on sensory data, cannot be fully replicated
    testing is not enough
  Ariane 5, 1996 (integer overflow in inertial reference system routine)
    Environment
  Mars Pathfinder, 1997 (priority inversion, see Silberschatz)

## Slide 31: Take-Home Message
Tests, although necessary, allow only a partial verificaiton of system’s behaviour
Predictability must be improved at the kernel level
Overload handling and fault-tolerance
Critical systems must be designed by making pessimistic assumptions…
…Murphy’s laws
  If something can go wrong, it will go wrong
  If a system stops working, it will do it at the worst possible time
  Sooner or later, the worst possible combination of circumstances will happen…

## Slide 32: Achieving predictability
DMA
  Cycle stealing
  Possible solution: time-slice method
    each memory cycle split into two adjacent time slots
      one reserved for the CPU, the other for the DMA device
    more expensive than cycle stealing
      but more predictable

## Slide 33: Achieving predictability
Cache
  Hit ratio
    80% of times: hits
    20% of times: performance degrades
    Preemptive systems destroy locality
    Cache-related preemption delay difficult to precisely estimate

## Slide 34: Achieving predictability
Interrupts
  Source: peripheral devices
  Can introduce unbounded delays
  Handling routines with static priorities
    generic OS: I/O have real-time constraints
    RTOS: a control process could be more urgent than interrupt handling
  3 different approaches

## Slide 35: Achieving predictability
Interrupts
  Can introduce unbounded delays
Disable all interrupts, except the one from the timer; devices handled by application tasks using polling
 + predictability, kernel-independent; - efficiency
Disable all interrupts except the one from the timer; manage devices via periodic kernel routines
 + encapsulation; - overhead
Leave all interrupts enabled; minimize drivers’ size (only activates device management task)
 + no busy waiting; - (small) unbounded overhead due to drivers

## Slide 36: Achieving predictability
System Calls
  Could be difficult to evaluate worst-case execution time of each task
  All system calls should be characterized by bounded execution time
  Desirable that system calls be preemptable

## Slide 37: Achieving predictability
Semaphores
  Priority inversion
  Must be avoided!
  Several methods:
    Basic priority inheritance
    Priority ceiling

## Slide 38: Achieving predictability
Memory management
  Demand paging
  Solution: static partitioning
    memory segmentation rule with fixed memory management scheme
■ + predictability, - flexibility in dynamic environments

## Slide 39: Achieving predictability
Programming language
  Dynamic data structures
  Recursion
  Cycles
  High-level languages for programming hard real-time applications
    Real-Time Euclid
    Real-Time Concurrent C

## Slide 40: Modeling Real-Time Activities

## Slide 41: Task
Sequence of instructions that in the absence of other activities is continuously executed by the processor until completion.
 Note: “activation” = “arrival” = “request” = “release” time
Task i
activation time
start time
t
Ci
finishing time
computation
time
ai si fi
Ri
The interval fi  ai is referred to as the task response time Ri
CPU
activation
dispatching termination
Ready queue
3 2 1

## Slide 42: Schedule
A particular assignment of tasks to the processor that determines the task execution sequence. Formally:
Given a task set Γ={ τ1, …, τn }, a schedule is a function σ: R+  N that associates an integer k to each time slice [ti, ti+1) with the meaning:
  k=0: in [ti, ti+1) the processor is idle
  k>0: in [ti, ti+1) the processor executes τk
At times t1, t2,…: context switch
1 2 3
idle
idle
(t)
3
2
1
0
t
t3
t4
t1 t2

## Slide 43: Preemptive Scheduling
A running tasks may be suspended and placed in the ready queue
 + Exception handling: timely response to issues
 + Different levels of criticality: preemption executes most critical tasks
 + Higher efficiency (CPU utilization)
  - Destroys program locality
  - Introduces runtime overhead
priority
1
2
3
(t)
3
2
1
0
0
2
4
6
8 10 12 14 16 18 20
0
2
4
6
8 10 12 14 16 18 20

## Slide 44: Definitions
Definition: feasible schedule
  A schedule σ is said to be feasible if all the tasks can complete according to a set of specified constraints.
Definition: schedulable set of tasks
  A set of tasks Γ is said to be schedulable if there exists at least one
algorithm that can produce a feasible schedule for it.

## Slide 45: Real-Time Task
“Completion time” = fi - si = Ri – (si- ai)
Definition: feasible task
  A real-time task τi is said to be feasible if it completes within its absolute deadline, that is, if fi ≤ di, or, equivalently, if Ri ≤ Di.
t
fi
d
i
It is a task characterized by a timing constraint on its response time, called
deadline:
relative deadline Di
i
ai si
response time Ri
absolute deadline (di = ai + Ri)

## Slide 46: Slack and Lateness
Di
t
ai
si
fi
Ri
i
di
slacki = di - fi
Di
lateness
Li = fi - di
t
ai si
di fi
Ri
“Slack” if lateness is negative (task completes before deadline)
“Laxity” or “slack time” Xi = di – ai – Ci
“Tardiness” or “exceeding time” Ei = max( 0, Li )
i

## Slide 47: Tasks and Jobs
A task running several times on different input data generates a sequence of instances (jobs):
Job 1
i,1
Job 2
i,2
Job 3
i,3
ai,k
ai,k+1
t
i
Ci
ai,1

## Slide 48: Activation Mode
Time-driven
  Periodic tasks (τi)
  The task is automatically activated by the operating system at predefined time instants.
Event-driven
  Aperiodic tasks: “jobs” (Ji)
  The task is activated at an event arrival or by explicitly invocating a system call.

## Slide 49: Periodic Task
input
U
= Ci
C
i
computation time
sync
timer (period Ti )
output
utilization factor
Ti
i
A periodic task τi generates an infinite sequence of instances or jobs
(same code on different data): τi,1, τi,2, …, τi,k, …
Ti
Ci
i

## Slide 50: The IDLE State
dispatching
signal
wait
RUNNING
READY
terminate
activate
BLOCKED
Timer
wait_for_next_period
wake_up
IDLE
preemption

## Slide 51: Periodic Task
Ti
job ik
ai,k
ai,k+1
i (Ci , Ti , Di )
Ci
t
ai,1 = i
task phase
ai,k di,k
= i + (k1) Ti
= ai,k + Di
often
Di = Ti

## Slide 52: Exercise
9.51
Torroni, Real-Time Operating Systems M ©2013
Consider a periodic task τ1(C1,T1,D1) with phase Φ1, where:
  C1 = 10 ms, T1 = 50 ms, D1 = 25 ms, and Φ1 = 100 ms
What is τ1’s utilization factor?
Is τ1 feasible?
What is τ1,1’s absolute deadline?
What is τ1,1’s laxity?
What is τ1,2’s release time?
Can τ1,1 and τ1,2 have different laxity?
Can τ1,1 and τ1,2 have different slack?
If τ1,2’s slack is 10ms, what is τ1,s’s finishing time?
What is τ1,2’s response time?
With a 2-CPU machine, can τ1,2 and τ1,3 have the same release time?
Can τ1,2 and τ1,3 have the same finishing time?

## Slide 53: Aperiodic Task
Aperiodic:
ai,k+1 > ai,k
minimum interarrival time
Sporadic:
ai,k+1
 ai,k + Ti
Ci
job ik
Ci
Ci
ai,k
ai,k+1
t
i
ai,1

## Slide 54: Estimating Ci is Not Easy
?
# occurrencies
loop
?
?
Each job operates on different data and can take different paths.
Even for the same data, computation time
depends on the processor state (cache, prefetch queue, number of preemptions).
execution time
Ci
min
Ci
max
timer

## Slide 55: Predictability vs. Efficiency
# occurrencies
execution time
Ci
min
Ci
max
Ci
avg
Ci estimate
safe
efficient
unsafe

## Slide 56: Predictability vs. Efficiency
non-RT task SOFT task HARD task
efficiency predictability
Ci
min
Ci
max
Ci
avg
Ci

## Slide 57: Criticality and Value
It is a parameter related to the consequences of missing the deadline
  Hard: missing deadline may have catastrophic consequences
  Hard Real-Time System if it can handle hard tasks
    sensory acquisition
    low-level control
    sensory-motor planning
  Soft: missing a deadline causes performance degradation
    reading data from the keyboard—user command interpretation
    message displaying
    graphical activities
Value, vi = the relative importance of a task wrt other tasks

## Slide 58: Jitter
It is a measure of the time variation of a periodic event:
a1 t1
Absolute:
a2
t2 a3 t3
a4
max (tk – ak) – min (tk – ak)
k k
Relative:
max | (tk – ak) – (fk-1 – ak-1) |
k

## Slide 59: Types of Jitter
fi,1
Finishing-time Jitter
i
fi,2
fi,3
si,1
Start-time Jitter
i
si,1 si,2 si,3
Completion-time Jitter (I/O Jitter)
i
si,2
si,3
fi,2
fi,1
fi,3

## Slide 60: Task Constraints

## Slide 61: Types of Constraints
Timing constraints
  Activation, completion, jitter.
Precedence constraints
  They impose an ordering in the execution.
Resource constraints
  They enforce a synchronization in the access of mutually exclusive resources.

## Slide 62: Explicit Timing Constraints
Timing constraints can be explicit or implicit.
Explicit timing constraints
  Directly included in the system specifications.
Example:
  open the valve in 10 seconds
  send the position within 40 ms
  read the altimeter every 200 ms
  acquire the camera every 20 ms

## Slide 63: Implicit Timing Constraints
They do not appear in the system specifications…
  but need to be met in order to satisfy the performance requirements
Example
  What is the validity of a sensory data?
t0
?

## Slide 64: Computing the Yellow Duration
D ≥ Td + Tr + Tb
  Td = Detection time
  Tr = Reaction time
  Tb = Braking time ~ v / .5 g
Td = .8s, Tr = .8s, v = 50 km/h (14 m/s)  D ≥ ???
vmax???
STOP

## Slide 65: Precedence Constraints
Sometimes tasks must be executed with specific precedence relations, specified by a Directed Acyclic Graph (Precedence Graph):
Immediate predecessor
Predecessor

## Slide 66: Sample Application
Tasks:
  Acquisition (acq1, acq2)
  Edge detection (edge1, edge2)
  Shape detection (shape), pixel disparities (disp)
  Height determination (height), recognition (rec)
Precedence graph?
stereo vision
processing
recognition

## Slide 67: Precedence Graph
acq1
acq2
edge1
edge2
shape
disp
depth
rec

## Slide 68: Resource Constraints
To preserve data consistency, shared resources must be accessed in
mutual exclusion:
x = 3
y = 5
W
R
x = 1
y = 8
x = 1
y = 5
W
R
x=1
y=8
read

## Slide 69: Mutual Exclusion
However, mutual exclusion introduces extra delays:
x = 3
y = 5
x = 1
y = 8
x = 1
y = 8
W
R
x = 1
y = 8
W
R

read

## Slide 70: Definition of Scheduling Problems

## Slide 71: General Scheduling Problem
Given:
  a set of n tasks, Γ = {τ1, τ2, …, τn}
    a precedence graph
    a set of timing constraints associated with each task
  a set of m processors, P = {P1, P2, …, Pm}
  a set of s types of resources, R = {R1, R2, …, Rs}
find an assignment of P and R to Γ which produces a feasible schedule.
Scheduling algorithm
 P R

feasible

## Slide 72: Scheduling Complexity
In 1975, Garey and Johnson showed that the general scheduling problem is NP hard.
  There is no known polinomial time algorithm
  Meaning:
    Consider n = 30 tasks; elementary step = 1μs
    Alg. 1: O(n)
    Alg. 2: O(n6)
    Alg. 3: O(6n)
    Computation time?
However, polynomial time algorithms can be found under particular conditions

## Slide 73: Simplifying Assumptions
Simplify architecture
  Single processor
Homogeneous task sets
  Only periodic / only aperiodic
Fully preemptive tasks
Simultaneous activations
No precedence constraints
No resource constraints
…
Different classes of algorithms

## Slide 74: Algorithm Tassonomy
Preemptive vs. Non Preemptive
Static vs. Dynamic
On-line vs. Off-line
Optimal vs. Heuristic
Guaranteed vs. Best-effort
Clairvoyant algorithm

## Slide 75: Static vs Dynamic
Static scheduling algorithms
  scheduling decisions are taken based on fixed parameters, statically assigned to tasks before activation.
Dynamic scheduling algorithms
  scheduling decisions are taken based on parameters that can change with time.

## Slide 76: Off-line vs. On-line
Off-line scheduling algorithms
  all scheduling decisions are taken before task activation: the schedule is stored in a table and later executed by a dispatcher
    “table-driven scheduling”
On-line scheduling algorithms
  scheduling decisions are taken at run-time on the set of active tasks
    When?

## Slide 77: Optimal vs. Heuristic
Optimal scheduling algorithms
  They generate a schedule that minimizes a cost function, defined based on an optimality criterion.
Heuristic scheduling algorithms
  They generate a schedule according to a heuristic function that tries to satisfy an optimality criterion, but there is no guarantee of success.

## Slide 78: Guaranteed vs. Best Effort
Guaranteed scheduling algorithms
  They generate a feasible schedule if there exists one
  Needed is hard real-time
  Pessimistic assumptions
Best effort scheduling algorithms
  No guarantee of a feasible schedule.
  Useful if soft real-time
  Optimize average performance

## Slide 79: Guarantee-Based Algorithms
In hard real-time applications, the feasibility of the schedule must be guaranteed before task execution
  Give the system time to try and avoid catastrophic consequences
  Look-ahead and worst-case reasoning
Static real-time systems: guarantee off-line; table-based scheduling
 + Run-time overhead does not depend on complexity of scheduling algorihtm
  - Flexibility
Dynamic real-time systems: task can be created at run-time
  Guarantee online every time a new task is created

## Slide 80: Guarantee Mechanism
BLOCKED
READY
RUNNING
dispatching
termination
wait
signal
preemption
ACTIVE
Worst-case assumption: a task could unnecessarily be rejected
  - Efficiency
Early detection of potential overload situation
 + Avoid negative effects (possible catastrophe, domino effect)
acceptance test
activation
YES
NO

## Slide 81: Domino Effect

## Slide 82: Metrics for Performance Evaluation
Classical operating systems
Optimality: min cost function
  Average response time
  Total completion time
  Weighted sum of completion times
  Maximum lateness
  Maximum number of late tasks
  …
Real-Time Operating Systems: these cost functions are not necessarily of interest
  No individual assessment of timing properties (periods, deadlines)
  Maximum lateness has no direct relation with number of tasks that miss their deadline

## Slide 83: Maximum Lateness
Min maximum lateness
Min number of tasks that miss their deadline

## Slide 84: Cumulative Value
Sum of the utility functions computed at each completion time
ai
fi
v (fi)
non real-time soft real-time
ai
di
f
i
v (fi)
ai
di
fi
hard real-time
v (fi)
v (fi)
ai di
-
“better never than late”
fi
on-time
“firm”

## Slide 85: Scheduling Anomalies

## Slide 86: A Surprising Result…
Theorem (Graham, 1976)
If a task set is optimally scheduled on a multiprocessor with some priority assignment, a fixed number of processors, fixed execution times, and precedence constraints, then increasing the number of processors, reducing execution times, or weakening the precedence constraints can increase the schedule length
Brittleness of scheduling algorithms: small changes can have big, unexpected consequences

## Slide 87: Richard’s Anomalies (Graham, 1976)
Assume a parallel machine with 3 CPU. All tasks arrive at the same time.
What priority-based schedule?
How to improve schedule length?
T9: 9
T8: 4
T1: 3
T2: 2
T3: 2
T4: 2
T7: 4
T6: 4
T5: 4
priority
Pi > Pj  i < j

## Slide 88: 1) Increase number of CPUs
Assume 4 CPUs
T9: 9
T8: 4
T1: 3
T2: 2
T3: 2
T4: 2
T7: 4
T6: 4
T5: 4
priority
Pi > Pj  i < j

## Slide 89: 2) Reduce computation time
Reduce computation time of each task by 1 unit
T9: 9
T8: 4
T1: 3
T2: 2
T3: 2
T4: 2
T7: 4
T6: 4
T5: 4
priority
Pi > Pj  i < j

## Slide 90: 3) Weaken precedence constraints
Remove constraints on T7 and T8
T9: 9
T8: 4
T1: 3
T2: 2
T3: 2
T4: 2
T7: 4
T6: 4
T5: 4
priority
Pi > Pj  i < j

## Slide 91: Another Surprising Result…
If tasks share mutually exclusive resources, or are non-preemptive, scheduling anomalies may also occur in uniprocessor systems
Theorem (Buttazzo, 2006)
A real time application that is feasible on a given processor can become infeasible when running on a faster processor
1
2
What if double the processor’s speed?

## Slide 92: Another Surprising Result…
If tasks share mutually exclusive resources, or are non-preemptible, scheduling anomalies may also occur in uniprocessor systems
Theorem (Buttazzo, 2006)
A real time application that is feasible on a given processor can become infeasible when running on a faster processor
What if double the processor’s speed?

## Slide 93: A dangerous operation: DELAY
A delay(Δ) may introduce a delay greater than Δ
1
2
0
8
10
12
14
2 4
delay(2)
6
blocked
1
2
0
2
4
6
8
10
12
14

## Slide 94: A dangerous operation: DELAY
A delay(Δ) may also increase the response times of other tasks
  Example for fixed priorities
1
2
0
10
15
0
4
8
12
5
delay(1)
deadline miss
1
1
2
0
5
10
15
0
4
8
12

## Slide 95: A dangerous operation: DELAY
A delay(Δ) may also increase the response times of other tasks
  Example for deadline scheduling
deadline miss
1
2
15
4
12
0
8
16
16
15
4
12
0
8
1
2
delay(8)

## Slide 96: Take-Home Message
Tests are not enough for real-time systems
Intuitive solutions do not always work
Delay should not be used in real-time tasks
The safest approach:
  Use predictable kernel mechanisms
  Analyze the system to predict the behaviour
The operating system is the part most responsible for a predictable behavior. Concurrency control must be enforced by:
  appropriate scheduling algorithms
  appropriate syncronization protocols
  efficient communication mechanisms
  predictable interrupt handling