## Slide 1: CSCI1600: Embedded and Real Time Software
Lecture 27: Real Time Scheduling II
Steven Reiss, Fall 2016

## Slide 2: Rate Monotonic Scheduling
Consider (8,4) , (10,2) , (12,3)
  Utilization = 0.5 + 0.2 + 0.25 = 0.95
  RM fails: (WHY)
  Are the tasks schedulable?

## Slide 3: Dynamic Priority Scheduling
Priorities are changed dynamically for different tasks
  Otherwise same simplifying assumptions
Approaches to assigning priorities
  Basic idea: give priority to the job that needs it the most
  Least laxity (least slack) first
  Earliest deadline first

## Slide 4: Least Laxity First
Laxity = time until deadline – compute time remaining
  This is a measure of how stressed we are to finish the job
  Small laxity implies high priority

## Slide 5: Least Laxity Scheduling
(8,4) , (10,2) , (12,3)
  0 :Laxity = 4, 8, 9
  1 : Laxity = 4, 7, 8
  2 : Laxity = 4, 6, 7
  3 : Laxity = 4, 5, 6
  4 : Laxity = X, 4, 5
  5 : Laxity = X, 4, 4
  6 : Laxity = X, X, 3
  7 : Laxity = X, X, 3
  8 : Laxity = 4, X, 3
  9 : Laxity = 4, X, X
  10 : Laxity = 4, 8, X
  11 : Laxity = 4, 7, X
  12 : Laxity = X, 7, 9 …

## Slide 6: Least Laxity First
Is optimal
  Can schedule as long as utility is <= 1
Is complex
When do priorities change
  The laxity of a task changes dynamically
    If it is not currently executing
  How would you implement this
Generally not used
  Too much context switching, bookkeeping
  Can we approximate it?

## Slide 7: Earliest Deadline First (EDF)
Put tasks in priority queue based on actual deadline
  Time when job needs to be done
Priorities change only when a job is added
EDF is also optimal
  If the utility is <= 1 then EDF will create a schedule
  Can transform any feasible schedule into an EDF one
But this is based on assumptions
  Perfect periodic tasks, zero overhead, independence

## Slide 8: Earliest Deadline First Scheduling
(8,4) , (10,2) , (12,3)
  0 : [8,10,12]
  8 : [ 10, 12, 16]
  10 : [ 12, 16, 20 ]

## Slide 9: EDF Scheduling
  P1(4,1), P2(6,3), P3(10,3)
Why is this sufficient?

## Slide 10: EDF Seems Ideal
Easy to implement, optimal, …
But only in an ideal world
  If the workload is briefly non-schedulable
    Then both fail dramatically and unpredictably
  Choices are based on deadlines, not importance
    Work hard to display MPG rather than firing airbag
Work only with idealized situations
  We need to relax the simplifying conditions
Sporadic and aperiodic tasks

## Slide 11: Handling Overloads
Why bother
  Tasks might take longer than expected
  Sporadic tasks (interrupts, etc.)
  Might be unavoidable
In EDF if one job is late and the system is loaded
  Then ALL future jobs might be late
Techniques
  What might you want to do?

## Slide 12: Techniques for Handling Overload
Techniques
  Schedule late jobs at lower priority than on-time jobs
  Change non-critical jobs to optional when late jobs occur
  Discard jobs that cannot complete
Tradeoffs
  What are the effects of each of these
  What might you use in practice
    Depends on application

## Slide 13: Relaxing Constraints
Non-preemptability
Resource Contention
Self-suspension
Context Switching time
Sporadic and aperiodic jobs
Job dependencies
Multiple cores/threads/processors

## Slide 14: Relaxing Non-Preemptability
Compute maximum time a task might be non-preemptable
Compute maximum time a task might be delayed
  By a non-preemptable task
  Only need to consider tasks of lower priority
Add this to its execution time when deriving schedule

## Slide 15: Resource Contention
Recall what can happen with locks and priorities
  Even without deadlock and race conditions
  Can have priority inversions

## Slide 16: Priority Protocols
τ2
τ3
t
0
t+3
t+253
R
L L L R
R L
τ1
t+254
L L L
...
L L
Blocked!
t+2

## Slide 17: Fixing Priority Inversions
Make critical sections non-preemptable
  This works, but …
  Critical tasks can be delayed

## Slide 18: Immediate Priority Ceiling Protocol
Assign priorities based on resources
Associate a priority ceiling p with each resource r
  The highest priority task that can lock it
No task with priority >= p is allowed to lock r
Task acquiring r runs at priority p

## Slide 19: Priority Inheritance Protocol
Priority inheritance protocol
  If Ti blocks Tk, execute Ti with priority min(i,k)
  Change priority of a task someone is blocked by it
Which should you use?

## Slide 20: Handling Self-Suspension
Why would this ever happen?
  Wait for I/O operations, etc.
Split into two tasks
  Second task might have a shorter deadline
  Take the suspension time into account when computing schedule

## Slide 21: Handling Context Switching Time
Compute the max # of context switches for a task
  From its period and higher priority tasks
  Worst case
Add the context switching time * max
  To the execution time of the task

## Slide 22: Sporadic Tasks
Sporadic tasks
  Arise occasionally
  Hard deadlines
Question: how to schedule these
  How to accommodate in RM/DM or EDF schedules
Goal
  Tell accept/reject when job is submitted
  If accepted, then job will meet its deadline

## Slide 23: Sporadic Jobs and EDF Schedules
EDF will find a schedule as long as U <= 1
  Keep track of U for the current system
    Utilization of the periodic tasks
    Plus the U for all accepted sporadic tasks
Compute U’ as current U plus U of the sporadic task
  If this is <= 1 then accept
  Otherwise reject

## Slide 24: Sporadic Jobs and RM Schedules
What guarantees can we make here?
  U <= x where x depends on the number of tasks
This allows us to use the same approach
  Just check with <= X for appropriate X

## Slide 25: Homework
Read 12.5
  Exercise 12.5

## Slide 26: Aperiodic Job Scheduling
Aperiodic Tasks
  Arise occasionally
  Soft deadlines
  Might be prioritized
Goal: minimize worst/average case performance

## Slide 27: Simple Aperiodic Scheduling
Run aperiodic tasks in open slots
How to schedule them
  Round robin
  Prioritized round robin
    Run tasks with higher priorities first
    Allocate CPU time according to priority
This gives no guarantees of performance
  And complicates the scheduler

## Slide 28: Priority Ceiling Protocol
Original Priority Ceiling Protocol
  Task’s priority is raised when a higher-priority task tries to acquire the lock
    Raised to priority ceiling of the resource
  Task can acquire a lock r only if the task’s priority is strictly higher than the priority ceilings of all locks currently held by other tasks